## Slide 1: WHMIS
The Basics

## Slide 2: Overview
Under WHMIS, workers have the right to receive information about each controlled product they use – its identity, hazards, and safety precautions. The goal of WHMIS is to reduce injury and disease by communicating specific health and safety information about controlled products so that the information can be used to reduce exposure to hazardous materials.
The Workplace Hazardous Materials Information System (WHMIS) provides information about many hazardous materials used in the workplace. WHMIS calls these hazardous materials controlled products.

## Slide 3: Federal & Provincial/Territorial WHMIS Legislation
The Federal WHMIS legislation came into effect on October 30, 1988 under the Hazardous Products Act and four other pieces of federal legislation.
Controlled Products
Ingredient Disclosure List
Hazardous Materials Information Review Act
Hazardous Materials Information Review Regulations
WHMIS came into effect in Ontario on October 31, 1988 as a Regulation under the Occupational Health and Safety Act (OSHA).
In Ontario, the WHMIS Regulation applies to all workplaces that are covered by the OHSA and is enforced by the Ministry of Labour.
The federal workplaces are inspected by Labour Canada, which enforces WHMIS under its jurisdiction.

## Slide 4: 3 Basic Elements of WHMIS
WHMIS Labels: Labels on controlled products alert workers to the identity of the product, hazards, and precautionary measures.
Material Safety Data Sheets (MSDS): Technical bulletins provide detailed hazard and precautionary information.
WHMIS Education and Training: The employer provides education and training for workers so that they can work safely with and near controlled products. Workers need to know how WHMIS works, the hazards of controlled products in their workplace, and the safe work procedures they must follow.

## Slide 5: Key WHMIS Participants
Suppliers
  Classify all controlled products
  Supply proper labels and MSDS
  Keep information on labels and MSDS current
Employers
  Educate and train workers
  Provide safe work procedures
  Ensure availability of proper up-to-date labels and MSDS
Workers
  Understand content and significance of labels and MSDS
  Follow safe work procedures and WHMIS requirements
  Notify employers about problems with labels and MSDS
RESPONSIBILITIES

## Slide 6: WHMIS Elements
WHMIS controlled products are classified by their hazard. There are six hazard classes and eight hazard symbols that identify the specific hazards. (There are three symbols in Class D.) The eight hazard symbols identify the specific hazards of controlled products.

## Slide 7: CLASS A Compressed Gases
Gas under pressure
  Examples: butane, propane, acetylene, and fire extinguishers
Hazards
If a pressurized container is punctured because it is dropped or exposed to excessive heat, the exploding fragments or rocket-like projectiles present a serious physical hazard.
Heat may cause container to explode
Container may explode if dropped.

## Slide 8: CLASS B Flammable and Combustible Materials
May catch fire or explode Examples: acetone, isopropyl alcohol, stoddart solvent
Hazards
Flammables are more dangerous than combustibles because they ignite more easily. During use, they must be kept away from ignition sources such as sparks or open flames. When not in use, they must be stored in fire-resistant cabinets or other specified storage areas.

## Slide 9: CLASS C Oxidizers
Products causing or contributing to the combustion of other materials
  Examples: hydrogen peroxide, potassium nitrate, sodium chlorate
Hazards
Oxidizing materials greatly increase the risk of fire if they come in contact with materials that can burn. They should never be stored near flammable or combustible materials.

## Slide 10
CLASS D Poisonous and Infectious Materials
This class has 3 divisions: D1, D2 and D3.

## Slide 11: Class D1 Materials causing immediate and serious toxic effects
  Poisonous, may be fatal
  Examples: arsenic, methylene chloride, formaldehyde
Hazards
May be fatal if inhaled, swallowed or absorbed through skin
May burn skin or eyes upon contact

## Slide 12: Class D2 Materials Causing Other Toxic Effects
Poisonous, but not immediately dangerous to health
Chronic health effects on body orgrans, cardiovascular or nervous system
  Examples: carcinogens (asbestos, crystalline silica, benzene) sensitizers (methyl methacrylate) embroyotoxin (xylene)
Hazards
Repeated exposure may cause death or permanent injury.
May be a skin irritant or sensitizer causing allergic reaction.
May cause birth defects, cancer, reproductive problems, or impairment of body organs and systems.

## Slide 13: Class D3 Biohazardous Infectious Material
  May cause serious disease, resulting in death or illness
  Classifed as Risk Groups II, III or IV as defined by the Medical Research Council of Canada
  Examples include: commercial cultures containing infectious organisms such as HIV, Ebola, and Hepatitis B
Hazards
Microorganisms (includes viruses, bacteria, fungi) can cause disease in persons and animals. They may be present in cultures. Products containing biohazardous infectious materials may be found in laboratory and research facilities associated with the medical or agricultural sectors.

## Slide 14: CLASS E Corrosive Materials
Caustics or acids causing severe irritation and burns to skin or eyes
  Examples: sodium hydroxide, bleach, hydrochloric acid, hydrofluoric acid
Hazards
Corrosive materials can cause permanent damage (e.g., burns) to skin and eyes.
May be harmful if inhaled.
May eat through metal.

## Slide 15: CLASS F Dangerously Reactive Materials
Products that can undergo dangerous reaction if subject to heat, light, pressure, shock, water, air
  Examples: hydrogen cyanide, vinyl acetate, chlorine dioxide
Hazards
Products in this class are very unstable . They can undergo vigorous polymerization reaction on their own, or become self-reactive when exposed to shock or to increase in pressure or temperature. It also includes products that react vigorously with water to release a toxic gas.

## Slide 16: WHMIS Labels
WHMIS Labels
The purpose of labels is to alert workers to the main hazards of controlled products and provide instructions for safe handling, and to direct workers to the MSDS for more information.
All WHMIS controlled products must be labelled
There are 2 types of WHMIS Labels
  Supplier Labels
  Workplace Labels
Other means of identification
  placards, warning signs, colour codes
Labels alert workers to hazards and safe handling instructions

## Slide 17: Supplier Label
Suppliers must provide supplier labels on containers of all controlled products sold or imported for use in the workplace.
Supplier labels will show seven types of information within the WHMIS hatched border.
The label must be clearly separated by a border to stand out from the container itself and other markings on the container (i.e., the size of the label should be appropriate for the size of the container).
Supplier Labels contain the following:
  Product name
  Hazard symbols
  Risk phrases
  Precautionary measures
  First aid measures
  Supplier identifier
  Reference to MSDS
All information must be disclosed in English and French within a hatched border

## Slide 18: Acceptable Format for the Supplier Label
Hazard Symbol(s)
Precautionary Statement(s)
Supplier Identifier
Product Identifier
First Aid Measures
Risk Phrases
Reference to the MSDS
Hatched Border

## Slide 19: Supplier Label Example

## Slide 20: Workplace Labels
Workplace labels are required on containers of controlled products produced on site, and on secondary containers where the product has been transferred from the original container.
Workplace labels are applied to:
  Secondary containers
  Containers of products received in bulk
  Employer-purchased products
  Containers with missing or illegible supplier labels
Workplace labels contain the following:
  Product name
  Safe handling procedures
  Reference to the MSDS

## Slide 21: Workplace Label Example
The format for workplace labels is flexible and may be in the language of choice in the workplace.

## Slide 22: MSDS Information
A Material Safety Data Sheet is a technical bulletin that provides specific hazard information, safe handling information, and emergency procedures for a controlled product. Since the MSDS contains detailed health and safety information specific to each controlled product, it should be used as a key source of information for developing training programs and safe work procedures. It is also a valuable reference source of health and safety information for workers, health and safety committees, and emergency service personnel.
The MSDS must be made available and accessible to all workers.

## Slide 23: Material Safety Data Sheet (MSDS)
A technical document providing information on a controlled product, for example:
  Hazardous ingredients
  Hazards (fire, explosion, reactivity)
  Health effects of exposure (acute and chronic)
  Hazard evaluation related to storage and handling
  Measures to protect workers
  Emergency procedures
Must be current (no more than 3 years old), complete, and readily available to workers

## Slide 24
Employers may use an electronic database to store MSDSs. In this case, it is essential that workers are provided information on accessing such a database to retrieve an MSDS. A hard copy of the MSDS should always be on hand when working with a controlled product in case electronic files are not accessible (e.g., the system is down).
Provides detailed information on the hazards of a controlled product
An important element for developing safe work procedures and control measures
A key element of worker education and training
Halton District School Board uses “MSDS Request” on MyHDSB to store electronic copies of all MSDS. Link: http://www.msdsforschools.ca/
Where to Find an MSDS

## Slide 25: Partial Exemptions
Some products are already covered by other labelling legislation and do not require WHMIS labels and MSDSs. However, Provincial legislation requires employers to educate and train workers about the hazards of partially exempt products, and safe work procedures. Partially exempt products still require Workplace Labels.
  Some Consumer Products
  Cosmetics
  Food and Drugs
  Medical Devices
  Radioactive Substances
  Pesticides
  Explosives
No WHMIS Supplier Label and MSDS Required
Education & Training and Workplace Labels Required

## Slide 26: Complete Exemptions
Completely Exempt
Some products are completely excluded from both Federal and Provincial WHMIS requirements. However, workers must be advised of hazards and be trained in safe handling procedures, as required under other provisions of the Occupational Health and Safety Regulation.
Wood and Products made of Wood
Manufactured Articles
Tobacco and Tobacco Products
Hazardous Wastes
Goods Handled Under TDG
  hazardous materials in transport
None of the WHMIS Requirements Apply
OH&S Regulation Applies

## Slide 27: WHMIS & Consumer Products
Consumer products are typically packaged and used for personal and household purposes. Suppliers and employers do not have to comply with the WHMIS label and MSDS requirements for consumer products, but workers must understand the hazards and safe use of them.
Although not legally required, most consumer products will have an MSDS available.
The obligation includes:
Ensuring that the worker has read and understood the consumer product labels.
Ensuring that the worker would recognize the different consumer product labels.
Ensuring that training is provided for the use, handling, storage and disposal of the consumer product(s).

## Slide 28: WHMIS & Consumer Products
Partial exemption of WHMIS applies to the following conditions:
The product must be packaged in a size normally available to consumers in a retail outlet.
The product must be available to the general public; wholesale outlets are not considered to be available to the public.
The product must be labelled to comply with the requirements for hazardous consumer products.
Health and safety precautions must still be taken.
The employer’s training obligations apply to any consumer product containing controlled substances used in a workplace.

## Slide 29: Consumer Product Labels
Labels on consumer products must appear in both English and French.
Hazard information must be clearly separated from the rest of the container by a border.
Most of the labels on products for consumer use sold in Canada meet the criteria set out for WHMIS workplace labels, namely:
The product is identified and the supplier / manufacturer’s name and address are included
Information is given on the safe handling of the product
Safety information is on the label, including: hazard warnings, instructions and directions for First Aid.

## Slide 30
Consumer Product Categories and Symbols
These are different from the WHMIS symbols.
There are five categories of consumer product symbols:
Category 1: Toxic or poisonous substances
The symbol used for all toxic materials is the skull & crossbones inside an octagonal border. The 8-sided border indicates “STOP” and take precautions listed on the label.
Category 2: Corrosive substances
The symbol used for all corrosive materials is the hand skeleton inside an octagonal border. The 8-sided border indicates “STOP” and take precautions listed on the label.
Category 3: Flammable substances
The symbol used for all flammable materials is a flame inside an octagonal border. The 8-sided border indicated “STOP” and take precautions listed on the label.
Category 4: Quick Skin Bonding Adhesive
Labels with specific warnings are required. The glue must be in a child-resistant container or enclosed in a child-resistant outer package. NO SYMBOL REQUIRED.
Category 5: Pressurized container
The products bearing this symbol either contain a liquid or gas under pressure. Consumer products bearing this symbol will include aerosol cans. The symbol used for all pressurized containers is an exploding image in a triangle or “WARNING”. Label with specific warnings is required.